## Slide 1
LMP: Light-Weighted Memory Protection with Hardware Assistance
Wei Huang, Zhen Huang, Dhaval Miyani and David Lie
University of Toronto
Presented by: Asmit De
CSE 544 Advanced System Security

## Slide 2: Motivation
2
CSE 544 Advanced System Security
Prevent memory corruption – ROP attacks
Existing CFI techniques are expensive and incur significant overheads (~ 2x)
Leverage Intel MPX hardware extensions to improve CFI performance
Contributions
Alternative usage of Intel MPX assisted pointer checker
Stack protection solution using Intel MPX
Low-overhead shadow stack implementation

## Slide 3: Intel MPX overview
3
CSE 544 Advanced System Security
Architectural components
  Bound registers
    BND0-BND3
  Configuration registers
    BNDCFGU and IA32_BNDCFGS
  Status register
    BNDSTATUS
  Bound management instructions
    BNDLDX and BNDSTX
    BNDMK and BNDMOV
  Bound check instructions
    BNDCU and BNDCL
Software Components
  MPX-enabled compiler
    MPX support in GCC v5.0+ for C/C++
  MPX runtime
    API to configure MPX features and manage MPX registers
  OS support
    Catch exceptions and signal applications
Notes: BND0-BND3: 128-bit, lower bound 64 bits and the upper bound 64 bits. Bound registers hold the upper and lower bounds that memory accesses are checked against.
BNDCFGU for user mode and IA32_BNDCFGS for supervisor mode.
BNDSTATUS stores error code when exception occurs.
BNDLDX and BNDSTX: Load/store BND registers from a table of object-speciﬁc address bounds in memory. 1000x NOP
BNDMK and BNDMOV allow a programmer to manually manage the BND registers.
BNDCU and BNDCL: If the pointer falls outside of the bounds, then the MPX hardware raises #BR exception (caught by MPX runtime), saving the need for an instruction to explicitly check the result of the comparison. 1x NOP
Compiler is responsible for inserting bound checks before pointer dereferences. Because bound information must be loaded in a limited number of BND registers before it can be used to check a pointer, the compiler must also load and spill bounds information between the BND registers and memory.

## Slide 4: Threat model and assumptions
4
CSE 544 Advanced System Security
Attacker can exploit memory corruption vulnerabilities to change values in arbitrary memory locations
Attacker is aware of the address locations of pointers, stacks, etc.
Attacker goal is to corrupt a code pointer to compromise program control flow
Attacker cannot directly modify CPU registers
Attacker cannot modify read-only memory pages
Attacker cannot compromise the loader or the OS
Forward-edge CFI protection is already in place to protect function pointers

## Slide 5: LMP Shadow Stack
5
CSE 544 Advanced System Security
Protect return boundaries by using a Shadow Stack
  Reserve a specific region of the address space for shadow stacks
  Allocate multiple shadow stacks contiguously for multi-threaded applications
  Dynamically allocate and map stack space from the reserved area when creating threads and their shadow stacks
  Use mapping table to store offset of a thread’s shadow stack from its actual call stack
  Partition the reserved area into fixed size shadow stacks and use a table to indicate which ones are active or free
  On thread creation, assign an unallocated shadow stack and update mapping table with the offset
  On thread destruction, deallocate its shadow stack and clear the offset in mapping table
Notes: As I mentioned on the MPX slide, the BNDLDX/STX instructions incur a significant overhead compared to just using the BND chk on the BND registers. The idea is to remove the use of bound table entirely and just use the bound registers. So we implement a shadow stack in a specific region….

## Slide 6: LMP Shadow Stack
6
CSE 544 Advanced System Security
Use MPX instructions to perform validation
  Instrument function entry code to save return address on the shadow stack
  Instrument function exit code to retrieve return address from shadow stack and place in a MPX BND register
  Use MPX bounds check instructions to compare return addresses with the BND register value
  MPX hardware raises #BR exception if comparison fails
  Better than compare/branch instruction in standard shadow stack implementation

## Slide 7: LMP Shadow Stack
7
CSE 544 Advanced System Security
Function assembly instrumentation
  On function entry
    Prepare shadow stack address in %rax
    Copy return address at %rsp to shadow stack
  Execute function body
  On function exit
    Copy return address from shadow stack to MPX bound register %bnd0
    Use bound checking instructions to compare return address at %rsp and %bnd0
  The location of the shadow stack is found by indexing into the stack region using the thread’s TID
  The return address from the shadow stack is set as both upper and lower bound in the bound register %bnd0
  Using BNDCU and BNDCL to compare instead of series of cmp/jmp instructions improves checking performance

## Slide 8: LMP Shadow Stack
8
CSE 544 Advanced System Security
Protect the Shadow Stack from attacks
  On program initialization, LMP runtime prepares the shadow stack memory region and saves its lower and upper bound addresses in BND1 register
  All memory store operations are instrumented using MPX instructions to prevent writing to shadow stack memory
  Write address is bounds checked with %bnd1 using BNDCU and BNDCL

## Slide 9: Performance overheads
9
CSE 544 Advanced System Security
Execution time
  3.9% avg. overhead
  12.55% max for h264ref (has significantly more function calls/rets)
  2.12% avg. overhead excluding h264ref
Code expansion
  39.27% avg. overhead
  Major contribution from bounds checking instructions
Overhead components
  Context settings: 0.1%
  Bounds checking: 0.52%
  Shadow stack ops: 3.27%
  84% of overheads is from shadow stack ops
  16% is from the memory protection system

## Slide 10
Presenter: Asmit De (aud311@psu.edu)
Image credits: All images used in this presentation belong to the authors of the original work, and have been used as-is from the source.
Thank You!